## Slide 1: Chapter 1: Roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks

## Slide 2: What’s the Internet:
Millions of connected computing devices: hosts or end systems running network apps
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
  Private intranet restrict the flow of messages to and from the network
Protocols: control sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 3: What’s the Internet: “nuts and bolts” view
Communication links
  Fiber, copper, radio, satellite
  Transmission rate = bandwidth
Routers: forward packets (chunks of data)
ISP: provide a variety of different types of network access to the end systems
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 4: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks

## Slide 5: A closer look at network structure:
Network edge: applications and hosts
Network core:
  Routers
  Network of networks
Access networks, physical media: communication links

## Slide 6: The network edge:
End systems (hosts):
  Run application programs
    E.g. Web, email
  At “edge of network”
Client/server model
  Client host requests, receives service from ‘always-on’ server
    E.g. Web browser/server; email client/server
Peer-peer model:
  Minimal (or no) use of dedicated servers
  E.g. Gnutella, kazaa

## Slide 7: Network edge: connection-oriented service
Goal: data transfer between end systems
handshaking: setup data transfer ahead of time
  Hello, hello-back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
Reliable, in-order byte-stream data transfer
  Loss: acknowledgements and retransmissions
Flow control:
  Sender won’t overwhelm receiver
Congestion control:
  Senders “slow down sending rate” when network congested

## Slide 8: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]:
  connectionless
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (Web), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, DNS, Internet telephony

## Slide 9: Chapter 1: Roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks

## Slide 10: The Network Core
Mesh of interconnected routers
The fundamental question: how is data transferred through net?
  Circuit switching: dedicated circuit per call: telephone net
  Packet-switching: data sent thru net in discrete “chunks”

## Slide 11: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 12: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 13: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 14: Network Core: Packet Switching
Each end-end data stream divided into packets
Packets of user A and B share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
Congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 15: Packet Switching: Statistical Multiplexing
Statistical multiplexing: A multiplexing technique that allows information from a number of channels to be combined for transmission over a single channel.
This is an alternative to creating a fixed sharing of a link, such as in TDM, where each host gets same slot in a TDM frame.
A
B
C
10 Mb/s
Ethernet
1.5 Mb/s
D
E
Sequence of A & B packets does not have fixed pattern
queue of packets
waiting for output
link

## Slide 16: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link
In above fig. : delay =???
3L/R
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay ??
R
R
R
L

## Slide 17: Packet-switched Networks: Forwarding
Goal: move packets through routers from source to destination
Datagram network:
  Destination address in packet determines next hop
  Routes may change during session
  Analogy: driving, asking directions
Virtual Circuit network:
  Each packet carries tag(virtual circuit ID): tag determines next hop
  Fixed path determined at call setup time, remains fixed thru call
  Routers maintain per-call state

## Slide 18: Network Taxonomy
Telecommunication
networks
Circuit-switched
networks
FDM
TDM
Packet-switched
networks
Networks
with VCs
Datagram
Networks
Datagram network is not either connection-oriented
or connectionless.
Internet provides both connection-oriented (TCP) and
connectionless services (UDP) to apps.

## Slide 19: Event Timing

## Slide 20
Fig. 18.1
Effect of packet size

## Slide 21: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks

## Slide 22: Physical Media
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5: 100Mbps Ethernet

## Slide 23: Physical Media: coax, fiber
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channel on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 5 Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 24: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
  2Mbps, 11Mbps
wide-area (e.g., cellular)
  e.g. 3G: hundreds of kbps
satellite
  up to 50Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 25: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks

## Slide 26: Internet structure: network of networks
Roughly hierarchical
At center: “tier-1” ISPs (e.g. AT&T), national/international coverage
A tier 1 network is a network that can reach every other network on the Internet without purchasing IP transit or paying for peering
  Treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)

## Slide 27: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 28: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 29: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 30: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks

## Slide 31: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 32: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queuing
  Time waiting at output link for transmission
  depends on congestion level of router

## Slide 33: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 34: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 35: THANK YOU